## Slide 1
Shared Memory Pool for Representors
William Tu, Michal Swiatkowski, and Yossi Kuperman
Nvidia and Intel
NetDev 0x18, 2024
Paper: https://github.com/williamtu/netdevconf18-sharedmem

## Slide 2: Switchdev Mode
Fast Path
An embedded switch in NIC
Legacy mode supports basic L2 features (mac/vlan)
Switchdev supports advanced hardware offloads
Vports (VFs/SFs) are switchdev ports and connected to VM
Handle most of the traffic in hardware
Notes: switch

## Slide 3: Switchdev Mode
Slow-Path
Runs on host, or in SmartNIC embedded CPU
Each vport has its own representor port (repr)
Repr is the control plane of the vport (representee)
Reprs attached to OVS or Linux bridge
Handles first couple packets of a connection
Insert/delete/update rules into switchdev

## Slide 4: Slow-Path Design Challenges
When creating thousands of SFs/VFs:
Each VF/SF has its own representor netdev, 1:1 mapping
Each representor netdev has its own RXQs, TXQs
Challenges
NIC does not have enough hardware queues
  ICE supports up to 1K queues
Consume too much memory
  Memory is not enough on SmartNIC
Do we need a dedicated netdev for
just handling slow path traffic?
Notes: Thousands of VMs/Containers, with 4:1 or 8:1 vcpu to pcpu oversubscription

## Slide 5: Slow-Path Design Challenges
When creating thousands of SFs/VFs with representors:  Design-0: Dedicated repr netdev
Each VF/SF has its own representor netdev, 1:1 mapping
Each representor netdev has its own RXQs
Challenges | Solutions
NIC does not have enough hardware queues | Design-1: Shared RXQs
Consume too much memory | Design-2: Adjustable RXQ for dedicated repr netdev
Notes: Thousands of VMs/Containers, with 4:1 or 8:1 vcpu to pcpu oversubscription

## Slide 6: Design-1: Shared RXQ
Solve the Hardware Queues Limitation
Don’t allocate any RXQs for representors
Shared RXQ for all representors
RX completion metadata indicates the incoming source vport id
TX can also use shared TXQ
Used by ice, nfp, sfc
Huge memory and queue saving

## Slide 7: Design-1: Fairness Issue
Sharing causes Starving!
Assume traffic all goes into slow-path
VM1 runs DPDK-pktgen
VM2 runs ping
All the buffers of shared RXQs are used by VM1
VM2 get zero slow-path bandwidth 
No performance isolation
Why not use tc policing/shaping? Backpressure?

## Slide 8: Slow-Path Design Challenges
When creating thousands of SFs/VFs with representors:  Design-0: Dedicated Repr netdev
Each VF/SF has its own representor netdev, 1:1 mapping
Each representor netdev has its own RXQs
2nd Challenge
Challenges | Solutions
NIC does not have enough hardware queues | Design-1: Shared RXQs
Consume too much memory | Design-2: Adjustable RXQ for dedicated repr netdev
Notes: Thousands of VMs/Containers, with 4:1 or 8:1 vcpu to pcpu oversubscription

## Slide 9: Experiment (1/2)
How much memory a mlx5 representor netdev consumes?
Create 200 SF-rep
Setup RXQs and UP:
Get memory differences
for i in {100..200}; do
devlink port add pci/0000:08:00.0 flavour pcisf pfnum 0 sfnum $i
done
for i in {100..200}; do
ethtool -L $dev combined 1 // number of channel/rxq
ethtool -G $dev rx 1024 // RXQ depth
ip link set dev $dev up
done
$ sar –r 1
04:51:08 PM kbmemfree kbavail …
04:51:09 PM 31179532 31321476

## Slide 10: Experiment (2/2)
How much memory a mlx5 representor netdev consumes?
FW pages
Page pool:
/proc/slabinfo, meminfo
/sys/kernel/debug/mlx5/0000\:08\:00.0/pages/fw_pages_total
./tools/net/ynl/cli.py --spec Documentation/netlink/specs/netdev.yaml --dump page-pool-get
{'id': 20,
'ifindex': 10,
'inflight': 448, // pages
'inflight-mem’: 1,835,008, // bytes
'napi-id': 518},

## Slide 11: MLX5 Representor Memory Consumption
1-RXQ, with 1024 RXQ depth: 2.86MB
Page pool consumes 1.83MB out of 2.86MB
2 channels is around double: 5MB
 | 1 RXQ total (MB) | Kernel Page Pool (MB) per-RXQ | FW (MB) | 2 RXQs (MB)
Q128 | 1.1 | 0.2 | 0.113 | 2.835
Q256 | 1.3 | 0.4 | 0.114 | 2.915
Q512 | 1.805 | 0.78 | 0.114 | 2.99
Q1024 | 2.86 | 1.83 | 0.114 | 5.025
Q2048 | 4.935 | 3.93 | 0.115 | 9.25
Can we allocate less RXQ buffers?

## Slide 12: Background: RXQ Buffer Pre-allocation
Why do we need RXQ buffers?
A NIC has multiple RXQs (circular rings)
Each RXQ has its own page pool, for re-allocating new pages after processing
Pre-allocates buffers for
  Handling burstiness, or
  Per-packet processing jitters
  NAPI schedule delay
Per-RXQ Page Pool
diff color

## Slide 13: Quick Evaluation (1/2)
Fixed High Watermark
Two servers connected back-to-back, single iperf TCP throughput
Hardware offload disabled, all traffic go to slow-path OVS
Statically change representor’s RXQ depth (ethtool –G rx) from 64 to 2048
What if there is no / little traffic?

## Slide 14: Design-2: Adjustable RXQ
save memory by dynamic allocation
Currently
Driver always refill rxq to full, ex: default 1024 buffers
Performance drop if rxq depth is too shallow, ex: 64
But what if there is little traffic? Then we waste lots of memory
…
…
…
…
Current: always refill to full
Repr1 Repr2 Repr-N
Notes: net/mlx5e: Remove the outer loop when allocating legacy RQ WQEs Legacy RQ WQEs are allocated in a loop in small batches (8 WQEs). As partial batches are allowed, there is no point to have a loop in a loop, so the outer loop is removed, and the batch size is increased up to the total number of WQEs to allocate, still not smaller than 8. Signed-off-by: Maxim Mikityanskiy <maximmi@nvidia.com>
[216820.772591] mlx5_core 0000:08:00.0: END mlx5e_post_rx_wqes: cur_sz 1024 1024 count(allocated) 256
[216849.765036] mlx5_core 0000:08:00.0: mlx5e_post_rx_wqes: head 256 tail 512 wqe_bulk 256 cur q sz 768 in_napi 0
[216849.767590] mlx5_core 0000:08:00.0: END mlx5e_post_rx_wqes: cur_sz 1024 1024 count(allocated) 256
[216849.770092] mlx5_core 0000:08:00.0: mlx5e_post_rx_wqes: head 256 tail 512 wqe_bulk 256 cur q sz 768 in_napi 0
[216849.772585] mlx5_core 0000:08:00.0: END mlx5e_post_rx_wqes: cur_sz 1024 1024 count(allocated) 256
[216853.841038] mlx5_core 0000:08:00.0: mlx5e_post_rx_wqes: head 512 tail 768 wqe_bulk 256 cur q sz 768 in_napi 0
[216853.843448] mlx5_core 0000:08:00.0: END mlx5e_post_rx_wqes: cur_sz 1024 1024 count(allocated) 256

## Slide 15: Design2: Dedicated Repr netdev with Adjustable RXQ
save memory by dynamic allocation
Currently
Driver always refill rxq to full, ex: default 1024 buffers
Performance drop if rxq depth is too shallow, ex: 64
But what if there is little traffic? Then we waste lots of memory
Idea: Don’t always allocate to full rxq size  save memory!
Performance impact: First burst of traffic greater 128 definitely lost
Low watermark set to fixed 128 buffers (2*NAPI_BUDGET)
High watermark, max RXQ buffers, set by ethtool –G rx
…
…
…
…
Current: always refill to full
Repr1 Repr2 Repr-N
low
watermark
128
…
…
…
…
Propose: dynamic refill
Repr1 Repr2 Repr-N
high
watermark
Notes: net/mlx5e: Remove the outer loop when allocating legacy RQ WQEs Legacy RQ WQEs are allocated in a loop in small batches (8 WQEs). As partial batches are allowed, there is no point to have a loop in a loop, so the outer loop is removed, and the batch size is increased up to the total number of WQEs to allocate, still not smaller than 8. Signed-off-by: Maxim Mikityanskiy <maximmi@nvidia.com>
[216820.772591] mlx5_core 0000:08:00.0: END mlx5e_post_rx_wqes: cur_sz 1024 1024 count(allocated) 256
[216849.765036] mlx5_core 0000:08:00.0: mlx5e_post_rx_wqes: head 256 tail 512 wqe_bulk 256 cur q sz 768 in_napi 0
[216849.767590] mlx5_core 0000:08:00.0: END mlx5e_post_rx_wqes: cur_sz 1024 1024 count(allocated) 256
[216849.770092] mlx5_core 0000:08:00.0: mlx5e_post_rx_wqes: head 256 tail 512 wqe_bulk 256 cur q sz 768 in_napi 0
[216849.772585] mlx5_core 0000:08:00.0: END mlx5e_post_rx_wqes: cur_sz 1024 1024 count(allocated) 256
[216853.841038] mlx5_core 0000:08:00.0: mlx5e_post_rx_wqes: head 512 tail 768 wqe_bulk 256 cur q sz 768 in_napi 0
[216853.843448] mlx5_core 0000:08:00.0: END mlx5e_post_rx_wqes: cur_sz 1024 1024 count(allocated) 256

## Slide 16: Quick Evaluation (2/2)
Dynamically Adjust the RXQ Depth
Simple Algorithm:
When in NAPI-interrupt: save memory by not refill, or refill up to low_watermark
When in NAPI-busy: fallback to default behavior, driver refill to FULL
The first burst over 128 definitely drops, but we’ll catch up

## Slide 17: Design-2+: Adjustable RXQ with Shared Page Pool
Problem: The later-created representors might get no memory
Current: each RXQ (NAPI) has its own page pool
Propose: all RXQs use the same page pool
Challenge: Need to track each RXQ usage and need lock
Use for representors (shared single DMA device)
Fairness issue?

## Slide 18: Fairness with Shared Page Pool
Borrow the solution from hardware switch and devlink-sb interface
Shared Buffer in Hardware Switch
Each output port has a logical queue
The logical queue decides the budge/usage of the output port
Dynamic Threshold: adjust queue depth based on current usage
For switchdev
Logical queue -> RXQ
Port -> representor netdev
Shared Buffer -> shared page pool
Limit a port’s shared memory usage to :
Shared Memory Switch with
multiple output ports
…
Shared Buffer
port1
port2
portN
Dynamic Queue Length Thresholds for Shared-Memory Packet Switches
Sizing Router Buffers

## Slide 19: New Devlink Attribute: spool-mode
None, Basic (Shared RXQs), SPP (Shared Page Pool)
Limited by Memory/Queue -> use shared RXQs
Performance isolation is important -> use adjustable RXQs or dedicated
mode | Feature | Drivers
None | Design-0: Dedicated repr netdev | Octeontx2, mlx5
Basic | Design-1: Shared RXQs | ICE, BNXT, NFP, SFC
SPP | Design-2: Adjustable RXQ with shared page pool | WIP
# dedicated repr netdev, ex: Octeontx2, mlx5
$ devlink dev eswitch set pci/0000:08:00.0 mode switchdev spool-mode none
# Shared RXQ with PF, ex: ICE, nfp
$ devlink dev eswitch set pci/0000:08:00.0 mode switchdev spool-mode basic
# WIP
$ devlink dev eswitch set pci/0000:08:00.0 mode switchdev spool-mode spp
Notes: include/net/page_pool.h:#define PP_ALLOC_CACHE_SIZE 128
diff --git a/include/net/page_pool.h b/include/net/page_pool.h
index edcc22605842..a65346df8a13 100644
--- a/include/net/page_pool.h
+++ b/include/net/page_pool.h
@@ -64,7 +64,7 @@
* cache is already full (or partly full) then the XDP_DROP recycles
* would have to take a slower code path.
*/
-#define PP_ALLOC_CACHE_SIZE 128
+#define PP_ALLOC_CACHE_SIZE 512
#define PP_ALLOC_CACHE_REFILL 64
struct pp_alloc_cache {
u32 count;

## Slide 20
Performance Evaluation

## Slide 21: Evaluation-1: Static RXQ, 64 - 2048
Apache ab benchmark with 1 million requests 100 concurrency, with different RXQ depth
Disable hw-offload
Time to complete (sec): total time taken for completing the 1 million requests.
out of buffers (K): a firmware counter, rx out of buffer, re- porting number of packets dropped due to no RXQ buffer available.
Requests (K) / sec: average HTTP requests per seconds
Connection Time (ms) and SD: average connection time, including connect, processing, and waiting, of the 1 million connections and their standard deviation (SD).
Notes: Time to complete (sec): total time taken for completing the 1 million requests.
out of buffers (K): a firmware counter, rx out of buffer, re- porting number of packets dropped due to no RXQ buffer available.
Requests (K) / sec: average HTTP requests per seconds
Connection Time (ms) and SD: average connection time, including connect, processing, and waiting, of the 1 million connections and their standard deviation (SD).

## Slide 22: Evaluation-2: Static RXQ vs Adjustable RXQ
Apache ab benchmark with 1 million requests 100 concurrency, with different RXQ depth
Disable hw-offload
Out of buffers showing more packets are dropped
Higher jittering
Average time to complete is similar
Static RXQ
Adjustable RXQ
Definitely need more benchmark strategies
Notes: Time to complete (sec): total time taken for completing the 1 million requests.
out of buffers (K): a firmware counter, rx out of buffer, re- porting number of packets dropped due to no RXQ buffer available.
Requests (K) / sec: average HTTP requests per seconds
Connection Time (ms) and SD: average connection time, including connect, processing, and waiting, of the 1 million connections and their standard deviation (SD).

## Slide 23: Summary
Need your feedback!
Switchdev slow-path and fast-path
Dedicated Representor Netdev and Shared RXQs
Adjustable RXQ (vendor drivers) with shared page pool
Add new devlink eswitch attribute: spool-mode
More performance number and design in paper
Discussion
Can shared page pool used in fast-path virtual device?
How to model the performance of adaptive RXQ?

## Slide 24
Thank you!

## Slide 25
Backup Slides

## Slide 26: OFED: Uplink Rep’s RQ for all other RQs
Uplink RQ’s to service all RX packets destined for non-uplink representors (SF/VF/PF)
Control plane
Devlink enable at switchdev mode/ or disable
Maintain xarray for vport id to representor netdev struct
Data plane: Steering
Insert pet header of 8 bytes (2 bytes contains new ethertype)
Copy 2 bytes of source vport that is stored in reg_c0
Set uplink as destination vport
Data Plane: driver
Get vport id from rx buffer, lookup netdev struct using vport id
Strip the 8 bytes from SKB and patch the SKB with correct netdev

## Slide 27: Scaling uplink REP’s rx Queues
Targeting 1K SFs
No Shared RQ
each repr has its own rxq, ex: 2 channel/2 rxqs
1k representors has total 2k rxqs
Each rep’s flow through its own rxhash
With Shared RQ on BlueField-3
PF creates 16 rxqs (max limited by CPUs)
Traffic from all representors uses the same rxhash and decides which rxq
Idea: increase 16 to more, ex: 128
Lower the chance for hash collision, depth depends on NAPI scheduler
NAPI schedule natively provides fairness for each queue
16 queues with 1024 entries is different than 128 queues with 64 entries!
Can we hash based on vport_id? If yes, it’s the same as no-sharedrq
Existing ethtool controls everything, no extra knob needed?
rxhash
rxqs
Uplink-REP
...
Packets from all representors
RFC: https://git-nbu.nvidia.com/r/c/upstream/linux/+/1099459
rxhash
rxqs
REP1
rxhash
rxqs
REP2
rxhash
rxqs
REPn
...
No SharedRQ
Packets steered to its own TIR
SharedRQ
Notes: From Parav
I think of following.
All switches operating using outputing queuing method, i.e based on the output queue, it dequeues and switches the packet. In our case, a netdev rxq to be dequeued based on the output port. So each RQ resembles the output queue.
above #1 gives us the fairness in processing packets regardless of their burst of packets from one or multiple VMs.
TIR creation should be optimized to support the needed scale
A meter on the RMP or RQ ensures that a burst does not starve other VMs. (buffer fairness)