## Slide 1
Shared Memory Pool for Representors
William Tu, Michal Swiatkowski, and Yossi Kuperman
Nvidia and Intel
NetDev 0x18, 2024

## Slide 2: Switchdev Mode
Fast Path
An embedded switch in NIC
Legacy mode supports basic L2 features (mac/vlan)
Switchdev supports advanced hardware offloads
Vports (VFs/SFs) are switchdev ports and connected to VM
Handle most of the traffic in hardware

## Slide 3: Switchdev Mode
Slow-Path
Runs on host, or in SmartNIC embedded CPU
Each vport has its own representor port (repr)
Repr is the control plane of the vport (representee)
Reprs attach to OVS or Linux bridge
Handles first couple packets of a connection
Insert/delete/update rules into switchdev
Slow-Path

## Slide 4: Slow-Path Design Challenges
When creating thousands of SFs/VFs with representors:
Each VF/SF has its own representor netdev, 1:1 mapping
Each representor netdev has its own RXQs
Challenges
NIC does not have enough hardware queues
  ICE supports up to 1K queues
Consume too much memory
  Memory is not enough on BlueField SmartNIC or IPU
Do we need a dedicated netdev for
just handling slow path traffic?
Notes: Thousands of VMs/Containers, with 4:1 or 8:1 vcpu to pcpu oversubscription

## Slide 5: Slow-Path Design Challenges
When creating thousands of SFs/VFs with representors:  Design-0: Dedicated Repr netdev
Each VF/SF has its own representor netdev, 1:1 mapping
Each representor netdev has its own RXQs
Challenges
NIC does not have enough hardware queues  Design-1: Shared RXQ of PF
  Intel ICE supports up to 1K queues
Consume too much memory  Design-2: Adjustable RXQ (new)
  Memory is not enough on BlueField SmartNIC or IPU
Notes: Thousands of VMs/Containers, with 4:1 or 8:1 vcpu to pcpu oversubscription

## Slide 6: Design1: Shared RXQ of PF
Solve the Hardware Queues Limitation
Don’t allocate any RXQs for representors
Redirect all representor’s traffic to PF or uplink representor
PF reconstruct the original packet’s information, ex: vport id
Huge memory and queue saving
TX can also reuse/redirect to PF’s TX queue
Used by ice, nfp, sfc, mlx5(not upstream)

## Slide 7: Design1: Fairness Issue
Sharing causes Starving!
Assume traffic all goes into slow-path
VM1 runs DPDK-pktgen
VM2 runs ping
All the buffers of RXQs of PF are used by VM1
VM2 get zero slow-path bandwidth 
Why not use tc policing/shaping? Backpressure?

## Slide 8: Slow-Path Design Challenges
When creating thousands of SFs/VFs with representors:  Design-0: Dedicated Repr netdev
Each VF/SF has its own representor netdev, 1:1 mapping
Each representor netdev has its own RXQs
Challenges
NIC does not have enough hardware queues  Design-1: Shared RXQ of PF
  Intel ICE supports up to 1K queues
Consume too much memory  Design-2: Adjustable RXQ (new)
  Memory is not enough on BlueField SmartNIC or IPU
Notes: Thousands of VMs/Containers, with 4:1 or 8:1 vcpu to pcpu oversubscription

## Slide 9: Experiment (1/2)
How much memory a mlx5 representor netdev consumes?
Create 200 SF-rep
Setup RXQs and UP:
Get memory differences
for i in {100..200}; do
devlink port add pci/0000:08:00.0 flavour pcisf pfnum 0 sfnum $i
done
for i in {100..200}; do
ethtool -L $dev combined 1 // number of channel/rxq
ethtool -G $dev rx 1024 // RXQ depth
ip link set dev $dev up
done
$ sar –r 1
04:51:08 PM kbmemfree kbavail …
04:51:09 PM 31179532 31321476

## Slide 10: Experiment (2/2)
How much memory a mlx5 representor netdev consumes?
FW pages
Page pool:
/proc/slabinfo, meminfo
/sys/kernel/debug/mlx5/0000\:08\:00.0/pages/fw_pages_total
./tools/net/ynl/cli.py --spec Documentation/netlink/specs/netdev.yaml --dump page-pool-get
{'id': 20,
'ifindex': 10,
'inflight': 448, // pages
'inflight-mem’: 1,835,008, // bytes
'napi-id': 518},

## Slide 11: MLX5 Representor Memory Consumption
1-RXQ, with 1024 RXQ depth: 2.86MB
1K representors: 2.86GB
Page pool consumes 1.83MB out of 2.86MB
2 channels is around double: 5GB
 | 1 RXQ total | Kernel Page Pool (MB) RXQ | FW (MB) | 2 RXQs (MB)
Q128 | 1.1 | 0.2 | 0.113 | 2.835
Q256 | 1.3 | 0.4 | 0.114 | 2.915
Q512 | 1.805 | 0.78 | 0.114 | 2.99
Q1024 | 2.86 | 1.83 | 0.114 | 5.025
Q2048 | 4.935 | 3.93 | 0.115 | 9.25
Can we allocate less RXQ buffers?

## Slide 12: Background: RXQ Buffer Pre-allocation
Why do we need RXQ buffers?
A NIC has multiple RXQs (circular rings), usually number of cores
Pre-allocates a set of RXQ buffers for handling burstiness, or processing/ NAPI schedule delay
Each RXQ has its own Linux page pool, for re-allocating new pages after processing
  RXQ depth impacts performance!
The total memory consists of
  Buffer size * number of queues * queue depth: 4K * 4 * 1024 = 16MB
Per-RXQ Page Pool

## Slide 13: Quick Evaluation (1/2)
Fixed High Watermark
Two servers connected back-to-back, single iperf TCP throughput on CX-5
Hardware offload disabled, all traffic go to slow-path OVS
Statically change RXQ depth (ethtool –G rx) from 64 to 2048
What if there is no / little traffic?

## Slide 14: Design2: Adjustable RXQ
save memory by dynamic allocation
Currently
Driver always refill rxq to full, ex: default 1024 buffers
Performance drop if rxq depth is too shallow, ex: 64
But what if there is little traffic? Then we waste lots of memory
…
…
…
…
Current: always refill to full
Repr1 Repr2 Repr-N
high
watermark
Notes: net/mlx5e: Remove the outer loop when allocating legacy RQ WQEs Legacy RQ WQEs are allocated in a loop in small batches (8 WQEs). As partial batches are allowed, there is no point to have a loop in a loop, so the outer loop is removed, and the batch size is increased up to the total number of WQEs to allocate, still not smaller than 8. Signed-off-by: Maxim Mikityanskiy <maximmi@nvidia.com>
[216820.772591] mlx5_core 0000:08:00.0: END mlx5e_post_rx_wqes: cur_sz 1024 1024 count(allocated) 256
[216849.765036] mlx5_core 0000:08:00.0: mlx5e_post_rx_wqes: head 256 tail 512 wqe_bulk 256 cur q sz 768 in_napi 0
[216849.767590] mlx5_core 0000:08:00.0: END mlx5e_post_rx_wqes: cur_sz 1024 1024 count(allocated) 256
[216849.770092] mlx5_core 0000:08:00.0: mlx5e_post_rx_wqes: head 256 tail 512 wqe_bulk 256 cur q sz 768 in_napi 0
[216849.772585] mlx5_core 0000:08:00.0: END mlx5e_post_rx_wqes: cur_sz 1024 1024 count(allocated) 256
[216853.841038] mlx5_core 0000:08:00.0: mlx5e_post_rx_wqes: head 512 tail 768 wqe_bulk 256 cur q sz 768 in_napi 0
[216853.843448] mlx5_core 0000:08:00.0: END mlx5e_post_rx_wqes: cur_sz 1024 1024 count(allocated) 256

## Slide 15: Design2: Dedicated Repr netdev with Adjustable RXQ
save memory by dynamic allocation
Currently
Driver always refill rxq to full, ex: default 1024 buffers
Performance drop if rxq depth is too shallow, ex: 64
But what if there is little traffic? Then we waste lots of memory
Idea: Don’t always allocate to full rxq size  save memory!
Performance impact: First burst of traffic definitely lost
Low watermark set to fixed 128 buffers (2*NAPI_BUDGET)
High watermark, max RXQ buffers, set by ethtool –G rx
…
…
…
…
Current: always refill to full
Repr1 Repr2 Repr-N
low
watermark
128
…
…
…
…
Propose: dynamic refill
Repr1 Repr2 Repr-N
high
watermark
Notes: net/mlx5e: Remove the outer loop when allocating legacy RQ WQEs Legacy RQ WQEs are allocated in a loop in small batches (8 WQEs). As partial batches are allowed, there is no point to have a loop in a loop, so the outer loop is removed, and the batch size is increased up to the total number of WQEs to allocate, still not smaller than 8. Signed-off-by: Maxim Mikityanskiy <maximmi@nvidia.com>
[216820.772591] mlx5_core 0000:08:00.0: END mlx5e_post_rx_wqes: cur_sz 1024 1024 count(allocated) 256
[216849.765036] mlx5_core 0000:08:00.0: mlx5e_post_rx_wqes: head 256 tail 512 wqe_bulk 256 cur q sz 768 in_napi 0
[216849.767590] mlx5_core 0000:08:00.0: END mlx5e_post_rx_wqes: cur_sz 1024 1024 count(allocated) 256
[216849.770092] mlx5_core 0000:08:00.0: mlx5e_post_rx_wqes: head 256 tail 512 wqe_bulk 256 cur q sz 768 in_napi 0
[216849.772585] mlx5_core 0000:08:00.0: END mlx5e_post_rx_wqes: cur_sz 1024 1024 count(allocated) 256
[216853.841038] mlx5_core 0000:08:00.0: mlx5e_post_rx_wqes: head 512 tail 768 wqe_bulk 256 cur q sz 768 in_napi 0
[216853.843448] mlx5_core 0000:08:00.0: END mlx5e_post_rx_wqes: cur_sz 1024 1024 count(allocated) 256

## Slide 16: Quick Evaluation (2/2)
Dynamically Adjust the RXQ Depth
Simple Algorithm:
When in NAPI-interrupt: save memory by not refill, or refill up to low_watermark
When in NAPI-busy: fallback to default behavior, driver refill to FULL
The first burst definitely drops, but we’ll catch up
Looks like little difference?

## Slide 17: Design2+: Adjustable RXQ with Shared Page Pool
Problem: The later-created representors might get no memory
Current: each RXQ has its own page pool
Propose: all RXQs use the same page pool
Challenge: Need to track each RXQ usage and need lock
Use for representors (shared single DMA device) or virtual devices (veth)
Fairness issue?

## Slide 18: Fairness with Shared Page Pool
Borrow the solution from hardware switch and devlink-sb interface
Shared Buffer in Hardware Switch
Each output port has a logical queue
The logical queue decides the budge/usage of the output port
Dynamic Threshold: adjust queue depth based on current usage
For switchdev
Logical queue -> RXQ
Port -> representor netdev
Shared Buffer -> shared page pool
Limit a port’s shared memory usage to :
Shared Memory Switch with
multiple output ports
…
Shared Buffer
port1
port2
portN
Papers:
Dynamic Queue Length Thresholds for Shared-Memory Packet Switches
Sizing Router Buffers

## Slide 19: New Devlink Attribute: spool-mode
None, Basic (Shared RXQ of PF), SPP (Shared Page Pool)
Memory is important -> use shared RXQ
QoS is important -> use adjustable RXQ or dedicated
mode | Feature | Drivers
None | Design-0: Dedicated repr netdev | Octeontx2, mlx5
Basic | Design-1: Shared RXQ of PF | ICE, BNXT, NFP, SFC
SPP | Design-2: Adjustable RXQ with shared page pool | WIP
# dedicated repr netdev, ex: Octeontx2
$ devlink dev eswitch set pci/0000:08:00.0 mode switchdev spool-mode none
# Shared RXQ with PF, ex: ICE
$ devlink dev eswitch set pci/0000:08:00.0 mode switchdev spool-mode basic
Notes: include/net/page_pool.h:#define PP_ALLOC_CACHE_SIZE 128
diff --git a/include/net/page_pool.h b/include/net/page_pool.h
index edcc22605842..a65346df8a13 100644
--- a/include/net/page_pool.h
+++ b/include/net/page_pool.h
@@ -64,7 +64,7 @@
* cache is already full (or partly full) then the XDP_DROP recycles
* would have to take a slower code path.
*/
-#define PP_ALLOC_CACHE_SIZE 128
+#define PP_ALLOC_CACHE_SIZE 512
#define PP_ALLOC_CACHE_REFILL 64
struct pp_alloc_cache {
u32 count;

## Slide 20
Performance Evaluation

## Slide 21: Evaluation-1: Static RXQ, 64 - 2048
Apache ab benchmark with 1 million requests 100 concurrency, with different RXQ depth
Disable hw-offload
Time to complete (sec): total time taken for completing the 1 million requests.
out of buffers (K): a firmware counter, rx out of buffer, re- porting number of packets dropped due to no RXQ buffer available.
Requests (K) / sec: average HTTP requests per seconds
Connection Time (ms) and SD: average connection time, including connect, processing, and waiting, of the 1 million connections and their standard deviation (SD).
Notes: Time to complete (sec): total time taken for completing the 1 million requests.
out of buffers (K): a firmware counter, rx out of buffer, re- porting number of packets dropped due to no RXQ buffer available.
Requests (K) / sec: average HTTP requests per seconds
Connection Time (ms) and SD: average connection time, including connect, processing, and waiting, of the 1 million connections and their standard deviation (SD).

## Slide 22: Evaluation-2: Static RXQ vs Adjustable RXQ
Apache ab benchmark with 1 million requests 100 concurrency, with different RXQ depth
Disable hw-offload
Out of buffers showing more packets are dropped
Higher jittering
Average time to complete is similar
Static RXQ
Adjustable RXQ
Definitely need more benchmark strategies
Notes: Time to complete (sec): total time taken for completing the 1 million requests.
out of buffers (K): a firmware counter, rx out of buffer, re- porting number of packets dropped due to no RXQ buffer available.
Requests (K) / sec: average HTTP requests per seconds
Connection Time (ms) and SD: average connection time, including connect, processing, and waiting, of the 1 million connections and their standard deviation (SD).

## Slide 23: Conclusion and Future Work
Summary
Dedicated Representor Netdev
Shared RXQ of PF
Adjustable RXQ with shared page pool
Adding new devlink eswitch attribute: spool-mode

## Slide 24
Thank you!

## Slide 25
Backup Slides

## Slide 26: OFED: Uplink Rep’s RQ for all other RQs
Uplink RQ’s to service all RX packets destined for non-uplink representors (SF/VF/PF)
Control plane
Devlink enable at switchdev mode/ or disable
Maintain xarray for vport id to representor netdev struct
Data plane: Steering
Insert pet header of 8 bytes (2 bytes contains new ethertype)
Copy 2 bytes of source vport that is stored in reg_c0
Set uplink as destination vport
Data Plane: driver
Get vport id from rx buffer, lookup netdev struct using vport id
Strip the 8 bytes from SKB and patch the SKB with correct netdev

## Slide 27: Scaling uplink REP’s rx Queues
Targeting 1K SFs
No Shared RQ
each repr has its own rxq, ex: 2 channel/2 rxqs
1k representors has total 2k rxqs
Each rep’s flow through its own rxhash
With Shared RQ on BlueField-3
PF creates 16 rxqs (max limited by CPUs)
Traffic from all representors uses the same rxhash and decides which rxq
Idea: increase 16 to more, ex: 128
Lower the chance for hash collision, depth depends on NAPI scheduler
NAPI schedule natively provides fairness for each queue
16 queues with 1024 entries is different than 128 queues with 64 entries!
Can we hash based on vport_id? If yes, it’s the same as no-sharedrq
Existing ethtool controls everything, no extra knob needed?
rxhash
rxqs
Uplink-REP
...
Packets from all representors
RFC: https://git-nbu.nvidia.com/r/c/upstream/linux/+/1099459
rxhash
rxqs
REP1
rxhash
rxqs
REP2
rxhash
rxqs
REPn
...
No SharedRQ
Packets steered to its own TIR
SharedRQ
Notes: From Parav
I think of following.
All switches operating using outputing queuing method, i.e based on the output queue, it dequeues and switches the packet. In our case, a netdev rxq to be dequeued based on the output port. So each RQ resembles the output queue.
above #1 gives us the fairness in processing packets regardless of their burst of packets from one or multiple VMs.
TIR creation should be optimized to support the needed scale
A meter on the RMP or RQ ensures that a burst does not starve other VMs. (buffer fairness)

## Slide 28: Intel ICE driver
Both repr’s rx and tx are handled by PF repr
Currently no ECPF, only runs on host PF (wait for IPU)
TX
Goal: repr’s tx is sent to corresponding vport’s rx
Idea
“bypass” the steering block, tell the hardware to send directly to LAN or vport.
Steps
Repr call ice_xmit
Use skb->dst field to save vport id
Then dev_queue_xmit(skb)
Uplink tx xmit function set vport id in tx descriptor
ice_xmit_frame_ring() -> ice_eswitch_set_target_vsi()
Before Michal’s patch, a special “control plane vport” is created, with N queues assigned for N repr
With 1k SF, the control plane vport couldn’t create 1k queues -> move to shared queue design with PF
RX
Slow-path traffic handles by PF
Steps:
Redirect to uplink rep by seting rx descriptor id to uplink
Maintain xarray for vport id to repr netdev
Notes: https://patchwork.kernel.org/project/netdevbpf/patch/20240125125314.852914-4-michal.swiatkowski@linux.intel.com/
In ice we have a mechanism to "bypass" steering block. Using it we can tell the hardware to send the packet directly to LAN, or steer it to other vport. It is set in Tx descriptor. skb->dst field is used to pass the correct vport ID to uplink Tx function to allow this to happen. If you want to look at ice code: in ice_txrx.c file ice_xmit_frame_ring() -> ice_eswitch_set_target_vsi() in case operation mode is switchdev (we need this also for uplink Tx traffic to always go outside). in ice_eswitch.c file ice_eswitch_set_target_vsi() -> the descriptor is filled with correct data. ice_eswitch_port_start_xmit() -> the vport number is set in skb->dst based on netdev data struct.